## Slide 1: COMPUTER NETWORK

## Slide 2: AGENDA
Computer network
  Wan.man.lan.pan
Hardware
  network connecting device
  Network topology
Software
  OSI MODEL
  TCP/IP protocol
Window network command

## Slide 3: COMPUTER NETWORK
Computer networking
refers to interconnected computing devices that can exchange data and share resources with each other. These networked devices use a system of rules, called communications protocols, to transmit information over physical or wireless technologies.

## Slide 4: HARDWARE: NERTWORK CONNECTING DEVICE
L1 devices: repeater hub
L2 devices: bridge switch
L3 devices: router L3 – switch;L3 ASIC + L2 switch
L4 devices:
L7 devices:

## Slide 5: SWITCH VLAN

## Slide 6: SWITCH VLAN
A group of end stations and the switch ports that link them together make up a VLAN. The logical split may be justified for a variety of reasons, such as departmental or project membership. The end station and the port to which it is connected must both be members of the same VLAN in order for it to function physically.

## Slide 7: VLAN VIRTUAL LOCAL AREA NETWORK
Any broadcast domain that is divided and isolated in a computer network at the data connection layer is known as a virtual local area network (VLAN) (OSI layer 2). [2] [3] A physical object that has been replicated and changed by additional logic within a local area network is referred to in this context as virtual. In order to create the look and functioning of network traffic that is physically on a single network but behaves as though it is split between several networks, VLANs work by attaching tags to network frames and processing these tags in networking systems. Despite being connected to the same physical network, VLANs can maintain network application separation without the deployment of additional sets of cabling and networking hardware.

## Slide 8: NETWORK TOPOLOGY
The configuration of a communication network's components—links, nodes, etc.—is known as its topology. Network topology is a term used to define or explain the configuration of many forms of telecommunication networks, such as computer networks, industrial fieldbuses, and command and control radio networks.
The topological structure of a network is known as network topology, and it can be represented physically or conceptually. It is a graph theory application[3] where connecting devices are modeled as links or lines between the nodes, and communicating devices are modeled as nodes. Physical topology refers to where different network elements are located (such as device placement and cable installation), whereas logical topology shows how data moves throughout a network. Even if two networks may have different node distances, physical connections, transmission speeds, or signal kinds, their logical topologies might be the same. The physical layer of the OSI model is particularly interested in the physical topology of a network.

## Slide 10: OSI MODEL
The seven levels that computer systems employ to interact over a network are described by the Open Systems Interconnection (OSI) model. In the early 1980s, all significant computer and telecommunications businesses adopted it as the first universal architecture for network communications.

## Slide 11: OSI MODEL layer function
Layer 7: Application
End-user applications like web browsers and email clients operate at the application layer. It offers protocols that let computer programs transmit and receive data and give consumers useful information. The Hypertext Transfer Protocol (HTTP), File Transfer Protocol (FTP), Post Office Protocol (POP), Simple Mail Transfer Protocol (SMTP), and Domain Name System are a few examples of application layer protocols (DNS).
Layer 6: Presentation
Data is prepared for the application layer by the presentation layer. In order for data to be correctly received on the other end, it specifies how two devices should encode, encrypt, and compress data. Any data transmitted by the application layer is processed by the presentation layer before being delivered via the session layer.

## Slide 12
Layer 5: Session
The session layer establishes sessions, or channels of communication, between devices. It is in charge of starting sessions, making sure they are active and open while data is being exchanged, and shutting them down once communication is complete. The session layer can also establish checkpoints during a data transmission, allowing devices to pick up where they left off in the event that the session is terminated

## Slide 15: Mesh ‘LAN local area network

## Slide 16: COMPUTER NETWORK:SOFT WARE

## Slide 17: PHYSICAL

## Slide 18: TCP/ICP PROTOCOL SUITE
PICTURE

## Slide 19: HTTPS

## Slide 20: COMPUTER NETWORK: WINDOW COMMAND

## Slide 24
IP CONFIG
NESTRAT
PING

## Slide 25: COMPUTER NETWORK

## Slide 26: SCENARIO

## Slide 27: Tools nestat + task manager + taskkill